## Slide 1
Packet switching
Circuit Switching
Multiplexing: FDM and TDM

## Slide 2: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=

## Slide 3: Switching Techniques
In large networks there might be multiple paths linking sender and receiver. Information may be switched as it travels through various communication channels. There are two types of switching techniques
  Circuit Switching
  Packet Switching

## Slide 4: Circuit Switching
Circuit switching is a technique that directly connects the sender and the receiver in an unbroken path.
Telephone switching equipment, for example, establishes a path that connects the caller's telephone to the receiver's telephone by making a physical connection.
With this type of switching technique, once a connection is established, a dedicated path exists between both ends until the connection is terminated.
Routing decisions must be made when the circuit is first established, but there are no decisions made after that time.

## Slide 5: Circuit Switching
Circuit switching in a network operates almost the same way as the telephone system works.
A complete end-to-end path must exist before communication can take place.
The computer initiating the data transfer must ask for a connection to the destination.
Once the connection has been initiated and completed to the destination device, the destination device must acknowledge that it is ready and willing to carry on a transfer.

## Slide 6: circuit switching
end-end resources (buffers, link trans. rate) allocated to, reserved for “call” between source and destination
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
Used in Telephone networks

## Slide 7: Packet Switching
In packet switching methods, a message is broken into small parts, called packets.
Each packet is tagged with appropriate source and destination
addresses.
Since packets have a strictly defined maximum length, they
can be stored in main memory instead of disk, therefore access
delay and cost are minimized.
Also, the transmission speeds, between nodes, are optimized.
With current technology, packets are generally accepted onto
the network on a first-come, first-served basis. If the network
becomes overloaded, packets are delayed or discarded
(``dropped'').

## Slide 8: Packet Switching

## Slide 9: Packet switching
They do not necessarily travel together; they do not travel sequentially. They don't even all travel via the same route. But eventually they arrive at the right point -- that digital address added to the front of each string of digital data -- and at their destination are reassembled into the correct order

## Slide 10: Packet-switching: store-and-forward
packet transmission delay: takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
No resources are reserved. On demand switching.
Connectionless: No connection state is maintained by the routers in the path
Best effort delivery and individual packets may follow any path. E.g., Internet
source
R bps
destination
1
2
3
L bits
per packet
R bps
One-hop numerical example:
L = 10 Kbits
R = 100 Mbps
one-hop transmission delay = 0.1 msec

## Slide 11: Packet-switching: queueing
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for transmission over output link
Queueing occurs when work arrives faster than it can be serviced:

## Slide 12: Packet-switching: queueing
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for transmission over output link
Packet queuing and loss: if arrival rate (in bps) to link exceeds transmission rate (bps) of link for some period of time:
packets will queue, waiting to be transmitted on output link
packets can be dropped (lost) if memory (buffer) in router fills up

## Slide 13: Circuit switching Implementation: FDM and TDM
frequency
time
frequency
time
4 users
Frequency Division Multiplexing (FDM)
optical, electromagnetic frequencies divided into (narrow) frequency bands
Time Division Multiplexing (TDM)
time divided into slots
each call allocated its own band, can transmit at max rate of that narrow band
each call allocated periodic slot(s), can transmit at maximum rate of (wider) frequency band (only) during its time slot(s)

## Slide 15: Circuit switching (a numerical example)
For TDM: If the link can transmit/generate ‘f’ frames per second and each slot consists of ‘b’ bits, the transmission rate of each circuit is ‘f*b’ bits per second.
How long it takes to send a file of 640,000 bits from Host A to Host B over a circuit-switched network. Suppose that all links in the network use TDM with 24 slots and have a bit rate of 1.536 Mbps. Also suppose that it takes 500 msec to establish an end-to-end circuit before Host A can begin to transmit the file.
  Transmission rate = Link Rate or Bit rate / no. of slots = R/h bps
  Transmission time = size of file / transmission rate
  = x / (R/h) = (x*h)/R second
  Total time to send packet to destination = Transmission time + circuit setup time
Each circuit has a transmission rate of (1.536 Mbps)/24 = 64 kbps, so it takes (640,000bits)/(64 kbps) = 10 seconds to transmit the file. To this 10 seconds we add the circuit establishment time, giving 10.5 seconds to send the file

## Slide 16: Packet switching versus circuit switching
Advantages of packet switching:
  Great for ‘bursty’ data – sometimes data to send, but sometimes not.
  Resource can be shared.
  Simpler, no call setup.
Disadvantages:
  Excessive congestion possible: packet delay and loss due to buffer overflow
  protocols needed for reliable data transfer (TCP – Unit-3)
  congestion control (using TCP – Unit-3)
  No guaranteed service (does not mean its unreliable, it means you may or may not get bandwidth)
  Out-of-order delivery (reassembly at network layer – Unit-4)

## Slide 17: Packet switching versus circuit switching
Advantages of circuit switching:
  Great for constant traffic
  Minimal delay and loss
  Guaranteed service
Disadvantages:
  Sharing not possible so limited number of users can have access to link
  Call setup required which takes some time
  Resource idle if no data to send. (e.g. caller and callee are not talking and put the phone on hold)

## Slide 18: Packet switching versus circuit switching
Suppose a link capacity is 1Mbps and 10 users are there but only one user generates one thousand packets of size 1,000 bits each, while other users are totally inactive. Under TDM circuit switching, how much time will the active user need to send its data (i.e., one thousand packets of 1,000 bits each)?
  Each user will get only 100 Kbps (i.e., the circuit transmission rate).
  It needs to send 1,000,000 bits so time required = 1,000,000/100,000 = 10 seconds.
What about packet switching?
  Just 1 second

## Slide 19: Packet switching versus circuit switching
example:
1 Gb/s link
each user:
  100 Mb/s when “active”
  active 10% of time
Q: how many users can use this network under circuit-switching and packet switching?
*
N
users
1 Gbps link
…..
circuit-switching: 10 users

## Slide 20: How do packet delay and loss occur?
packets queue in router buffers, waiting for turn for transmission
  queue length grows when arrival rate to link (temporarily) exceeds output link capacity
packet loss occurs when memory to hold queued packets fills up
A
B
packet being transmitted (transmission delay)
packets in buffers (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 22
No Overload!

## Slide 23
Transient Overload
Not a rare event!
Queue

## Slide 24
Transient Overload
Not a rare event!
Queue

## Slide 25
Transient Overload
Not a rare event!
Queue

## Slide 26
Transient Overload
Not a rare event!
Queue

## Slide 27
Transient Overload
Not a rare event!
Queue

## Slide 28
Queue
Transient Overload
Not a rare event!
Queues absorb transient bursts!

## Slide 29
What about persistent overload?
Will eventually drop packets

## Slide 30: Packet delay: four sources
dproc: nodal processing
check bit errors
determine output link
typically < microsecs
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 31: Propagation and Transmission Delay
Propagation Delay = Distance/Propagation speed
Transmission Delay = Message size/bandwidth bps
Latency = Propagation delay + Transmission delay + Queueing time + Processing time

## Slide 32
What is the propagation time if the distance between the two points is 12,000 km? Assume the propagation speed to be 2.4 × 108 m/s in cable.
Solution
We can calculate the propagation time as
The example shows that a bit can go over the Atlantic Ocean in only 50 ms if there is a direct cable between the source and the destination.

## Slide 33: Packet delay: four sources
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different

## Slide 34: End-End Delay

## Slide 35: Caravan analogy
car ~ bit; caravan ~ packet; toll service ~ link transmission
toll booth takes 12 sec to service car (bit transmission time)
“propagate” at 100 km/hr
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr) = 1 hr
A: 62 minutes
toll booth
toll booth
(aka link)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
toll booth
toll booth
(aka link)
toll booth

## Slide 36: Caravan analogy
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, first car arrives at second booth; three cars still at first booth

## Slide 38: Timing in Circuit Switching
time

## Slide 39
time

## Slide 40
time
Timing in Circuit Switching

## Slide 41: Timing in Circuit Switching
time

## Slide 42
Circuit Establishment
time
Timing in Circuit Switching

## Slide 43
Information
Circuit Establishment
Transfer
time
Timing in Circuit Switching

## Slide 44
Information
Circuit Establishment
Transfer
Circuit Teardown
time
Timing in Circuit Switching
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 45: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”*
01000111100010101001110100011001
Internet Address
Age
Checksum to protect header
Header
Data
header
payload

## Slide 46: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”*
  payload is the data being carried
  header holds instructions to the network for how to handle packet (think of the header as an interface!)

## Slide 47: Packet Switching
Data is sent as chunks of formatted bits (Packets)
Packets consist of a “header” and “payload”
Switches “forward” packets based on their headers

## Slide 48: Switches forward packets
to MIT
to UW
UCB
to NYU
Destination | Next Hop
UCB | 4
UW | 5
MIT | 2
NYU | 3
Forwarding Table
111010010
MIT
switch#2
switch#5
switch#3
switch#4

## Slide 49: Timing in Packet Switching
time
payload
hdr
What about the time to process the packet at the switch?
We’ll assume it’s relatively negligible (mostly true)
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 50: Timing in Packet Switching
time
payload
hdr
Could the switch start transmitting as soon as it has processed the header?
Yes! This would be called a “cut through” switch
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 51: Timing in Packet Switching
time
payload
hdr
We will always assume a switch processes/forwards a packet after it has received it entirely. This is called “store and forward” switching
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 52: Packet queueing delay (revisited)
a: average packet arrival rate
L: packet length (bits)
R: link bandwidth (bit transmission rate)
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving is more than can be serviced - average delay infinite!
La/R ~ 0
La/R -> 1
traffic intensity = La/R
average queueing delay
1
service rate of bits
R
arrival rate of bits
L
a
.
:
“traffic
intensity”

## Slide 53: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
3 probes
3 probes
3 probes
  sends three packets that will reach router i on path towards destination (with time-to-live field value of i)
  router i will return packets to sender
  sender measures time interval between transmission and reply

## Slide 54: Real Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
* Do some traceroutes from exotic countries at www.traceroute.org
* means no response (probe lost, router not replying)
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
3 delay measurements
to border1-rt-fa5-1-0.gw.umass.edu
looks like delays decrease! Why?
trans-oceanic link

## Slide 55: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
A
B
packet being transmitted
buffer
(waiting area)
* Check out the Java applet for an interactive animation (on publisher’s website) of queuing and loss
packet arriving to
full buffer is lost
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all

## Slide 56: Nodes and Links
A
B

## Slide 57: Performance of a Network
Performance of a network pertains to the measure of service quality of a network as perceived by the user. There are different ways to measure the performance of a network, depending upon the nature and design of the network.
Bandwidth: This is about the volume of data that can be transferred over a network. The standard measurement for data transfer speed is megabits per second (Mbps).
Throughput: While bandwidth gives us how much data could theoretically be transferred across the network, throughput indicates how much data was actually transferred from a source at any given time.
Latency: It measures the time it takes for a data to get to its destination across the network. It is commonly measured as a round trip delay. Latency is usually measured in milliseconds (ms).

## Slide 58: Properties of Links
Bandwidth (capacity): “width” of the link
  number of bits sent (or received) per unit time (bits/sec or bps)
Latency (delay): “length” of the link
  propagation time for data to travel along the link (seconds)
Bandwidth-Delay Product (BDP): “volume” of the link
  amount of data that can be “in flight” at any time
  propagation delay × bits/time = total bits in link
bandwidth
Latency
delay x bandwidth

## Slide 59: Throughput
throughput: rate (bits/time unit) at which bits are being sent from sender to receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)

## Slide 60: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 61: Throughput: network scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/

## Slide 62: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
3 probes
3 probes
3 probes
  sends three packets that will reach router i on path towards destination (with time-to-live field value of i)
  router i will return packets to sender
  sender measures time interval between transmission and reply

## Slide 63: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
A
B
packet being transmitted
buffer
(waiting area)
* Check out the Java applet for an interactive animation (on publisher’s website) of queuing and loss
packet arriving to
full buffer is lost
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all

## Slide 65: Example: organization of air travel
a series of steps, involving many services
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
How would you define/discuss the system of airline travel?
end-to-end transfer of person plus baggage

## Slide 66: Example: organization of air travel
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
ticketing service
baggage service
gate service
runway service
routing service
layers: each layer implements a service
  via its own internal-layer actions (e.g., gate layer- loading and unloading)
  relying on services provided by layer below (e.g., takeoff/landing layer - runway-to-runway passenger transfer service)

## Slide 67: One more example…
Dear John,
Your days are numbered.
--Pat
CEO A writes letter to CEO B
  Folds letter and hands it to administrative aide
Aide:
  Puts letter in envelope with CEO B’s full name
  Takes to FedEx
FedEx Office
  Puts letter in larger envelope
  Puts name and street address on FedEx envelope
  Puts package on FedEx delivery truck
FedEx delivers to other company

## Slide 68: The Path of the Letter
CEO
Aide
FedEx
CEO
Aide
FedEx
Location
Fedex Envelope (FE)
Letter
Envelope
Semantic Content
Identity
“Peers” on each side understand the same things
No one else needs to
Lowest level has most packaging

## Slide 69: The Path Through FedEx
Truck
Sorting
Office
Airport
FE
Sorting
Office
Airport
Truck
Sorting
Office
Airport
Crate
Crate
FE
New
Crate
Crate
FE
Higher “Stack”
at Ends
Partial “Stack”
During Transit
Deepest Packaging (Envelope+FE+Crate)
at the Lowest Level of Transport
Highest Level of
“Transit Stack”
is Routing

## Slide 70: Protocol “layers” and reference models
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question: is there any hope of organizing structure of network?
and/or our discussion of networks?

## Slide 71: Why layering?
Approach to designing/discussing complex systems:
explicit structure allows identification, relationship of system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change in layer's service implementation: transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system

## Slide 72: Layered Architectures
The TCP/IP Model (Internet Protocol Stack)
OSI Reference Model

## Slide 73: Layered Internet protocol stack
application: supporting network applications
  HTTP, IMAP, SMTP, DNS
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
link
application
network
transport
physical
application
transport
network
link
physical

## Slide 74: Services, Layering and Encapsulation
source
transport-layer protocol encapsulates application-layer message, M, with transport layer-layer header Ht to create a transport-layer segment
  Ht used by transport layer protocol to implement its service
application
transport
network
link
physical
destination
application
transport
network
link
physical
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
Application exchanges messages to implement some application service using services of transport layer
M

## Slide 75: Services, Layering and Encapsulation
source
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
network-layer protocol encapsulates transport-layer segment [Ht | M] with network layer-layer header Hn to create a network-layer datagram
  Hn used by network layer protocol to implement its service
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services

## Slide 76: Services, Layering and Encapsulation
source
Ht
M
link-layer protocol encapsulates network datagram [Hn| [Ht |M], with link-layer header Hl to create a link-layer frame
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Link-layer protocol transfers datagram [Hn| [Ht |M] from host to neighboring host, using network-layer services
M
Ht
Hn
Hl
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services

## Slide 77: Services, Layering and Encapsulation
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
Ht
M
M
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
Ht
M
M
message
segment
datagram
frame
M
Ht
Hn
Hl

## Slide 78: Encapsulation: an end-end view
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
source
Ht
Hn
M
segment
Ht
datagram
destination
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
link
physical

## Slide 79: In the context of the Internet
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits

## Slide 80: Three Observations
Each layer:
  Depends on layer below
  Supports layer above
  Independent of others
Multiple versions in layer
  Interfaces differ somewhat
  Components pick which lower-level protocol to use
But only one IP layer
  Unifying protocol

## Slide 81: Layering Crucial to Internet’s Success
Reuse
Hides underlying detail
Innovation at each level can proceed in parallel
Pursued by very different communities

## Slide 82: Distributing Layers Across Network
Layers are simple if only on a single machine
  Just stack of modules interacting with those above/below
But we need to implement layers across machines
  Hosts
  Routers (switches)
What gets implemented where?

## Slide 83: What Gets Implemented on Host?
Bits arrive on wire, must make it up to application
Therefore, all layers must exist at host!

## Slide 84: What Gets Implemented on Router?
Bits arrive on wire
  Physical layer necessary
Packets must be delivered to next-hop
  Datalink layer necessary
Routers participate in global delivery
  Network layer necessary
Routers don’t support reliable delivery
  Transport layer (and above) not supported

## Slide 85: What Gets Implemented on Switches?
Switches do what routers do, except they don’t participate in global delivery, just local delivery
They only need to support Physical and Datalink
  Don’t need to support Network layer
Won’t focus on the router/switch distinction
  When I say switch, I almost always mean router
  Almost all boxes support network layer these days

## Slide 86: Simple Diagram
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
Notes: Why go up? Why not stay down in the lower levels?

## Slide 87: Logical Communication
Layers interacts with peer’s corresponding layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 88: Physical Communication
Communication goes down to physical network
Then from network peer to peer
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 89: Layer Encapsulation
Trans: Connection ID
Net: Source/Dest
Link: Src/Dest
Appl: Get index.html
User A
User B
Common case: 20 bytes TCP header + 20 bytes IP header + 14 bytes Ethernet header = 54 bytes overhead
Notes: Deepest level most header

## Slide 90: OSI - Open System Interconnection ISO – International Standards for Organizations
Two layers not found in Internet protocol stack!
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical
The seven layer OSI/ISO
reference model
ISO/OSI reference model

## Slide 92: Snell’s Law: Refraction, Critical Angle
It states how light ray reacts when it meets the interface of two media having different index of refraction.
When the light ray encounters a boundary separating two different media, part of the ray is reflected back into the same medium and other part is refracted or bent as it enters the second medium.

## Slide 93: Snell’s Law: Refraction, Critical Angle, TIR

## Slide 94: Snell’s Law (numerical example)
A beam of light going through a medium with an index of refraction of 1.14 has an angle of incidence of 48o with another medium. If the light wave is at a new angle of 39o, what is the index of refraction for the second medium?
Use Snell’s Law. Answer: 1.346

## Slide 95: Chapter 1: summary
We’ve covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, access network, core
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
layering, service models
Security (left for your specialization )
You now have:
context, overview, vocabulary, “feel” of networking
more depth, detail, and fun to follow!

## Slide 96: Some numerical Problems
Suppose that a user at a PC at one end of Canada sends a 1-Mbit file to a remote server on the other end over a data link operating at 64 kbps. Assume that we are using a fiber optic link with a propagation rate of the speed of light, approximately 3 * 108 m/sec, and that the distance is 4800 km.
(a) What is the overall network delay, i.e. time to transmit the file? (Ignore any processing or queueing delays.)

## Slide 97: Some numerical Problems
dtotal = dpropagation + dtransmission
dpropagation = distance/speed = 4800*103/3*108 = 0.016 seconds
dtransmission = length/rate = 106/64*103 = 15.625 seconds

## Slide 98: Some numerical Problems
2. Suppose you are downloading an MP3 file of 64 MB, the server has a transmission rate of Rs = 4 Mbps, and you have an access link of Rc = 2 Mbps. What is the throughput ? What is the overall network delay, i.e. time to transmit the file? (Ignore any processing or queueing delays.)
Throughput =min(Rs, Rc) = 2Mbps
Time to transmit the file = 64*8/2 = 256 seconds

## Slide 99: Some numerical Problems
3. What is the propagation time if the distance between the two points is 12,000 km? Assume the propagation speed to be 2.4 × 108 m/s in cable.
Propagation time = 12000*1000 / 2.4*108 = 50 ms

## Slide 100: Some numerical Problems
4. What are the propagation time and the transmission time for a 2.5-kbyte message (an e-mail) if the bandwidth of the network is 1 Gbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s.
Propagation time = 12000*1000 / 2.4*108 = 50 ms
Transmission time = 2500*8 / 109 = 0.02 ms
Message is short and the bandwidth is high, the dominant factor is the propagation time, not the transmission time. The transmission time can be ignored.

## Slide 101: Some numerical Problems
5. What are the propagation time and the transmission time for a 5 MB image if the bandwidth of the network is 1 Mbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s.
Propagation time = 12000*1000 / 2.4*108 = 50 ms
Transmission time = 5,000,000*8 / 106 = 40 s
Message is long and the bandwidth is less, the dominant factor is the transmission time, not the propagation time. The propagation time can be ignored.

## Slide 102: Some numerical Problems
6. What is the propagation time if the difference between two points is 12,000 KM. Assume that the propagation speed is at 2.4 × 108 m/s.
Speed = Distance / time
Time = 12000*1000 / 2.4*108 = 50 ms

## Slide 103: Some numerical Problems
6. What is the propagation time and transmission time for a 2.5KB message if bandwidth of network is 1 Gbps. Assume that the distance between sender and receiver is 12,000 KM.
(Homework)